SUNSPOT BABY

Summary

| Boat Style: | Multihull Cruiser (Sailing Catamaran) | Hull Material: | Fiberglass - Cored | Length: | 38' 0" |
| --- | --- | --- | --- | --- | --- |
| Builder: | Prout | Rig : | Cutter | Beam: | 18' 5" |
| Model: | Manta | Sail Area : | n/a | Draft: | 3' 10" |
| Keel: | Shoal | Rudders: | Skeg protected | Weight: | Approx 15,400 lbs |
| Staterooms: | 3 | Sleeps: | 6-7 | Heads: | 1 |
| Engine Make: | Volvo | Water: | 175 gallons | Fuel: | 118 gallons |
| Engines: | 2 | Engine Type: | Sail Drive, Diesel | Horse Power: | 28 each engine 56 total |
| Mast Height Above Water | ~51.5' | Generator | Honda 2000 | Hull # | 17 |

GENERAL:

BUILDER:	Prout Catamarans

Peter Scofield, Harrissmith, South Africa			YEAR BUILT: 1994

DESIGNER:	Prout Catamarans			MODEL:	Manta 38

L.O.A.:	38' 0"	L.W.L.: 35’	BEAM:	18' 5"	DRAFT:	3' 10"

NET TON: 	15,400 lbs	(7.7 tons)	HULL #:	17

REG./DOC. NO.:	USCG 1116690

OWNER:  	Mr. & Mrs. George Stateham	ADDRESS:	New Bern, NC

HAILING PORT:	Oriental, NC		REGISTERED PORT: Oriental, NC

NAVIGATION LIMITS:  Offshore Capable

VESSEL’S BERTH: Northwest Creek Marina, New Bern, NC

HULL:

DECKS:	Molded fiberglass with core material

SUPERSTRUCTURE:   Molded fiberglass with core material

TOPSIDES:	Molded fiberglass with core material

BOTTOM:	Molded fiberglass (solid)

KEEL:	Twin bilge keels	SKEG:  Skeg Protected Rudders

STEM:	Curved		STERN:  Sugar Scoops

FRAMES:	Partitions and bulkheads

FLOOR TIMBERS: Partitions and bulkheads

DECK BEAMS:	Molded decks

FASTENINGS:	Reinforced fiberglass and stainless steel

BULKHEADS:	Five partial

INTERIOR:	Vinyl overhead, teak veneer wall covering, teak trim, vinyl plank sole and Formica counter surfaces

MACHINERY:

NO./MAKE/TYPE: Two Volvo Diesel ~1500 hours since complete overhaul.

HP/RPM:	 28  @ 3200		NO. CYLS.:	Three

LOCATION:    	Beneath port and starboard aft stateroom berths

MODEL:	(P) 2003B-BT      (S) 2003B-BT	SERIAL:	(P) 23000 57395    (S) 23000 57399

YEAR:	1994

ENGINE BED:  	Fiberglass stringers	ENGINE COOLING SYSTEM:	Seawater

BLOWERS:	Operable		VENTILATION:	Good

FUEL FILTERS:	Shared Racor dual element, switchable primary and Bosch secondary

EXHAUST LINE:	Hose connected                               		COOLED:	Seawater

EXHAUST SILENCER:  Plastic water collector type mufflers

CONTROLS:	Morse cable

REDUCTION GEAR: Volvo Sail Drives	RATIO:	2.24

MODEL:	(P) S120C           (S) S120C	SERIAL:	(P) 2101059140    (S) 2101059186

PROPELLER: Two 15" diam x 13 LH 3-bladed aluminum part #850672	SPARES: One new, one used

PROPELLER SHAFTS: Stainless steel	STRUTS:	Sail Drive lower unit

PROPELLER PROTECTION:	Keel lower	RUDDER:	Skeg supported fiberglass

APPROXIMATE SPEED (KNOTS): 8.0 maximum under power

ELECTRICAL SYSTEMS:

SHORE POWER: 120v 30amp 60 cycle

BATTERIES:        Two 12-volt dedicated starting batteries. Four 6-volt golf cart batteries for house bank.

BATTERY LOCATION: Aft of each engine and beneath companionway step

GENERATOR: Honda 2000 portable generator

BATTERY CHARGING: Xantrex Marine 20 2000 watt charger/inverter new 2009

Two Heart Interface digital echo~chargers

LIGHTING:	12-volt DC

WIRING:	Thermoplastic and molded rubber

SWITCHBOARD:   Aft in salon

CIRCUIT BREAKERS:	Yes	FUSED:	Yes	GROUND:	Negative

TANKS:

FUEL:	Diesel		NO. & CAPACITY: Two approx. 118 gallons total

LOCATION:	Beneath cockpit grating and aft of generator

MATERIALS:	Stainless steel	FILLING LINES AND VENTS:	Hose connected

VENTED OVERBOARD:	Yes

FUEL VALVES:	Approved type	LOCATION:	At tank and at Racor fuel filter

FUEL LINES:	Approved flexible type

WATER TANKS, NO. & CAPACITY: Two  approx. 175 gallons total

LOCATION:   	Port and starboard aft in keels

MATERIALS:	Integral fiberglass

HOLDING TANKS: One 15 gallon

LOCATION:	Under forward double berth

MATERIALS:      	One piece plastic

POPANE TANKS, NO, & CAPCITY: Two 20 lb.

LOCATION:	Starboard in anchor chain locker

MATERIALS:	 Aluminum

FITTINGS AND EQUIPMENT:

DECK HARDWARE: Stainless steel and aluminum

MAIN SAIL TRACK: Strong track

DINGHY DAVITS: Stainless steel

HARD DODGER:  Molded fiberglass, factory installed

STEERING GEAR:  Hynautic hydraulic

GROUND TACKLE:  35 lb. CQR anchor with approx. 200> of 3/8A chain

Add: Danforth 22S anchor with approx. 40' of 3/8" chain and 200' of 3/4" nylon rode

ANCHOR WINDLASS: Lewmar V3 with manual retrieval option new 2011	DECK WINCHES: See list near end

VHF RADIO:	Icom IC-M56		RADAR:	Furuno 16-mile

AUTO PILOT:	Raymarine S60 with ST7000 control head		DEPTH FINDER:	Raymarine depth

GPS:	Raymarine C120 chart plotter		KNOTLOG:	Autohelm Speed

AIS:	Raymarine AIS (Automatic Ship Identification system)

MARINE SINGLE SIDEBAND RADIO: ICOM 802 (Marine SSB & HAM) with ICOM AT140 antenna tuner and isolated back stay antenna

SATELITE COMMUNICATION UNIT: Skymate satellite weather, e-mail, & position reporting system

OTHER ELECTRONICS:   See list

ANTENNAS:    	VHF, GPS (2), radar, AIS, Skymate, and insulated backstay for SSB

NAV./ANCHOR LIGHTS:   Electric		COMPASS:	Suunto

HORN:	Portable air

WATER MAKER:	Pur 40E

HOT WATER:	Bosch propane

BILGE PUMPS:     Four hand operated, 4 electric, and one electric automatic shower pump

SPARS & RIGGING:

MASTS:	Main (aluminum)	 BOOMS:	Main (aluminum)

STANDING RIGGING: 1 x 19 stainless steel wire	RUNNING RIGGING:   Dacron line

SAILS:	Main, jib, staysail, and asymmetrical Genicker

GALLEY:

LOCATION:	Mid-section of starboard hull

TYPE OF STOVE: Seaward two-burner propane stove Model 2277 new 2002

OVEN: 	Seaward propane Model 325 s/n 649146 - i02 New 2002

STOVE LINES:	Rubber hose

STOVE SHUT-OFFS:  At burners in line valve, solenoid,  and tank

REFRIGERATION:  Isotherm 12-volt DC refrigerator in galley and Isotherm 12-volt DC freezer in main saloon

SAFETY AND FIRE FIGHTING EQUIPMENT:

FLARES:	Yes

LIFE JACKETS:	Seven Type 2

LIFE RINGS:	Two Type IV horseshoe buoy

LIFE RAFTS:	EV 10 person

PORTABLE EXTINGUISHERS: Two type ABC one type BC

OTHER ELECTRONICS AND EQUIPMENT LIST

ACR 406MH Epirb (Emergency position indicating radio beacon)

Guest Model 2433P Galvanic Isolator

Dual bow anchor rollers

Full-length mast steps

Mainmast fore deck light

Echomax Radar reflector

Masthead tricolor navigation light with strobe

Two Siemens solar panels

Mack-Pak mainsail control for fully battened main sail.

12-volt Wind powered generator

Stainless steel charcoal BBQ grill

Stainless framework for solar panels/wind generator

Raw water wash down system on forward deck

Two jack lines

Harken jib and staysail furling systems

Autohelm Compass digital compass display

Raymarine Wind apparent wind speed/wind direction instrument

Emergency tiller

Raymarine C120 chart plotter

ICOM M802 SSB transceiver and tuner

Autohelm Multi display at navigation center

Seawater foot pump and spigot at galley sink

Fresh water hand pump at galley sink

Microwave oven

Sony AM/FM/CD stereo

Canvas covers: Mack-Pack for main sail (New 2002), life raft, BBQ grill, custom deck house shade awning, cockpit Bimini (New 2011), hatches, winches

Pur 40E water maker (1.5 gph) plumbed to supply fresh water tank or spigot at galley sink.

WINCHES

Cockpit

Two Harken #46 two speed self-tailing primaries

One Harken #42 two speed self-tailing reefing/multipurpose

Main Mast

Harken #32 two speed self-tailing halyard